## Slide 1
Sitting Posture Corrector App on Raspberry Pi Using Edge AI
ACM India Winter School on Edge AI – Hackathon Project
Pranav MR – BITS Goa
pranavmr0402@gmail.com
Shreyas Sankaran – BITS Goa
iamshreyas08@gmail.com
Ashwin Prashant Hariharan – IIT Madras
24f3100099@es.study.iitm.ac.in
Ronalda M – NIT Srinagar
ronalda_2022phacse005@nitsri.ac.in
Veningston K – NIT Srinagar
veningstonk@nitsri.ac.in
dia
EdgeAI Posture Corrector

## Slide 2: Problem
Works on-device
Single camera in a side view.
MoveNet (TFLite) estimates 17 body keypoints in real time.
A calibrated scoring module maps posture deviation to Score ∈ [0, 100]. Raises warning to indicate Good / Bad posture.
Moreover, we also suggest the reason for the bad posture to help identify corrective measures.
dia
EdgeAI Posture Corrector

## Slide 3: Problem
Posture refers to the natural way one holds their body.
In this project, we are analyzing desk posture, specifically through 2 parameters,
1
2
Neck Slouch Torso Slouch
through a side view camera and a Raspberry Pi.
Goal: Detect sitting posture in real time and provide actionable feedback using a 0–100 score and warning.
We also aim to track Focus Time and Idle Time and alert the user about the same.
dia
EdgeAI Posture Corrector

## Slide 4: System Overview
Figure 1: End-to-end pipeline for posture monitoring in side view: input video frames → MoveNet keypoint extraction → angle computation → posture prediction and score visualization.
dia
EdgeAI Posture Corrector

## Slide 5: Hardware & Deployment
Edge device: Raspberry Pi (camera)
Compute: On-device inference with tflite runtime
Privacy: Video stays local; only score/warning output leaves the pipeline
dia
EdgeAI Posture Corrector

## Slide 6: Pose Estimation with MoveNet
MoveNet outputs keypoints
KP = {(xi , yi , ci }17
i =1
where, xi , yi , ci are normalized coordinates and confidence. Interest points from head, shoulder, hip.
Figure 2: MoveNet Architecture
dia
EdgeAI Posture Corrector

## Slide 7: Calibration & Scoring Configuration [1/3]
Runtime & Keypoint Settings
Alert & Session Timing
Frame resolution: 640×480, frame rate: 30 FPS
Minimum keypoint confidence: cmin = 0.3 (ignore low-confidence joints) Time scaling for testing: TIME RATE = 30.0 (accelerated evaluation)
Bad posture alert after sustained deviation: 10 s Idle alert after continuous sitting/standing: 30 min Focus session minimum duration: 5 min
dia
EdgeAI Posture Corrector

## Slide 8: Calibration & Scoring Configuration [2/3]
Angle Calibration (Reference Ranges)
Neck angle (ear–shoulder–hip):
NECK MIN = 130◦, NECK OPT = 180◦, NECK MAX = 200◦
Torso angle (shoulder–hip–knee):
TORSO MIN = 45◦, TORSO OPT = 90◦, TORSO MAX = 135◦
Degrees change to count as head movement
Movement-change thresholds (to detect activity):
∆θhead ≥ 10◦, ∆θleg ≥ 10◦
dia
EdgeAI Posture Corrector

## Slide 9: Calibration & Scoring Configuration [3/3]
Final Posture Score (0–100)
Score = Wneck · Sneck + Wtorso · Storso,
Wneck = 0.5, Wtorso = 0.5
Good posture if Score ≥ 75
dia
EdgeAI Posture Corrector

## Slide 10
Video Demo
dia
EdgeAI Posture Corrector

## Slide 11: Algorithm Outline
1
Capture frame, preprocess to MoveNet input size. Run MoveNet inference → keypoints {(xi , yi , ci )}.
Apply confidence gating; compute head/shoulder/hip and other midpoints. Extract angle features: neck flexion, torso slouch.
Drive ALERT based on Score and hold time.
2
3
4
5
dia
EdgeAI Posture Corrector

## Slide 12: Resource Footprint (CPU & RAM)
Measure CPU utilization and RAM usage. Report peak RAM and average CPU load.
Figure 3: Memory Footprint (No Inference vs. With Inference)
dia
EdgeAI Posture Corrector

## Slide 13: End-to-End Dataflow of the Mobile App
1
Periodic Activity Logging on RPi - The posture monitoring pipeline runs continuously to record activity log every 10 seconds and append locally to CSV files to enable lightweight storage and offline availability.
2
3
Flask server running on Rpi serves this data as JSON responses using an custom API.
The Flutter-based Mobile App periodically requests the JSON data over the local network (Wi-Fi/hotspot), parses the response, and visualizes user activity in a dashboard.
Posture score trends over time,
Good vs. bad posture duration summaries,
End-to-End Data Flow
4
Pose & Scoring (RPi) → CSV Logs (every 10s) → Flask API (JSON) → Mobile App → Dashboard
dia
EdgeAI Posture Corrector

## Slide 14: Conclusion
EdgeAI posture corrector runs locally on Raspberry Pi with real-time feedback. Calibration enables robust scoring under a single camera view.
dia
EdgeAI Posture Corrector

## Slide 15: Future Work
Multi-view posture estimation (for true 3D triangulation).
Upgrade from single-person MoveNet to a multi-person pose pipeline (detect persons →
run pose per ROI)
Expand classes (e.g., asymmetric sitting, phone neck).
dia
EdgeAI Posture Corrector
15 / 16

## Slide 16
BBC News.
”Sitting straight ’bad for backs” (BBC News, 2006).
http://news.bbc.co.uk/2/hi/6187080.stm.
Yi-Lang Chen et. al.,
”Postural Variabilities Associated with the Most Comfortable Sitting Postures: A Preliminary Study”.
Healthcare (Basel), 6;9(12):1685, 2021.
https://doi.org/10.3390/healthcare9121685.
Yuri Kwon et. al.,
”The effect of sitting posture on the loads at cervico-thoracic and lumbosacral joints”.
Technol Health Care. 26(Suppl 1):409–418., 2018.
https://doi.org/10.3233/THC-174717.
Donald D et. al.,
”Sitting biomechanics Part I: Review of the Literature”.
Journal of Manipulative and Physiological Therapeutics, Vol 22(9), 594-609, 1999.
https://doi.org/10.1016/S0161-4754(99)70020-5.
dia
EdgeAI Posture Corrector
15 / 16

## Slide 17
Oana-Ruxandra Stincel et. al.,
”Assessment of Forward Head Posture and Ergonomics in Young IT Professionals – Reasons to Worry?”.
Med Lav. 114(1), 2023.
https://doi.org/10.23749/mdl.v114i1.13600.
David A Titcomb et. al.,
”Evaluation of the Craniovertebral Angle in Standing versus Sitting Positions in Young Adults with and without Severe Forward Head Posture”.
Int J Exerc Sci. 17(1):73–85., 2024.
https://doi.org/10.70252/GDNN4363.
Dae-Hyun Kim et. al.,
”Neck Pain in Adults with Forward Head Posture: Effects of Craniovertebral Angle and Cervical Range of Motion”.
Osong Public Health Res Perspect. 9(6):309–313, 2024.
https://doi.org/10.24171/j.phrp.2018.9.6.04.
Physio-Pedia.
dia
EdgeAI Posture Corrector

## Slide 18
”Craniovertebral angle”.
https://www.physio-pedia.com/Craniovertebral_angle.
dia
EdgeAI Posture Corrector
16 / 16

## Slide 19
Thank you!
Questions?
dia
EdgeAI Posture Corrector
16 / 16